## Slide 1: Western Power Hack-a-Gig
Team UnicorNN

## Slide 2
Team UnicorNN
Sofia Sibanic
Electrical Engineer (Western Power) looking to broaden her skillset and apply learnings from fast.ai.
Adrian Goldberg
Geophysicist (Santos) with >10 years programming and ~2 years deep learning experience.
Jordan Pratt
Data Strategy Analyst (Western Power) looking to expand personal skills.

## Slide 3: Our Overall Approach
Initial idea was to split the team in half and share learnings
Team members choose what they are interested in
We undertook both challenges, but only Part A of Challenge 2
Learnings captured on GitHub repository wiki
Queries and tasks managed via team Slack channel

## Slide 4: Challenge 1
Smart Meter Data

## Slide 5: Challenge 1 – Smart Meter Data
Approach
Findings
Key Learnings

## Slide 6: Our approach
Adrian interested in time series problems, chose challenge 1.
Understanding – explored problem, objectives and recommendations.
Research – literature and open source code for similar datasets
Data – created clean test, and train datasets
Selected RMSE metric as metric for all forecasts
Forecasting – tried 9 model types, simple though complex
Clustering – explored several methods – chose a novel approach.
Notes: Initially started on own but requested to join team UnicorNN
Createing a clean dataset took 80% of time for this project

## Slide 7: We found…
Inconsistencies in the acquisition data
A relationship between Acorn groups and
consumption patterns
Several methods to reasonably
accurately forecast 7 days ahead
Notes: Data inconsistencies: gaps, varying start/stop dates for smart-meter acquisition.

## Slide 8: We learnt…
Use a sample dataset first – then run on full dataset
LightGBM is robust, quick to run - good forecasting performance.
LSTM for forecasting half hourly data gives good results but is really slow.
Converting the energy consumption curves to images and using a Neural Network to cluster is relatively fast and is worth further exploration
Notes: - break the data down into a manageable size as quickly as possible -
– build models on this, then run the workflows on the larger dataset.
Clustering large time series datasets using kNN and dynamic time warping
is very compute intensive

## Slide 9: Challenge 2
Photovoltaic generation
PART A - Detection

## Slide 10: Overview
Define requirements
  Understand task
  Analyse data
  Form an approach
  Consider limitations
  Determine deliverables
Follow to-do list (right)
Document learnings
Share insights
1
Retrieve Data
2
3
Explore Data
Prepare Data
4
Develop model
5
Assess performance
6
Submit Model

## Slide 11: Requirements (Part A)
The task
  Utilise Western Power data to develop a model which identifies distribution embedded PV generation. Target a model accuracy of >98.5%.
  Test what works, what doesn’t work – document learnings
  Assess model performance
  Provide required documents

## Slide 12: Approach
Understand Data
  What is provided?
Clean Release
  High degree of assumed PV and Non-PV image labelling accuracy
  Smaller set
Extra Release
  Lower degree of confidence in labelling accuracy
  Larger set (2-4x)

## Slide 13: Approach
Understand Data
  What does it tell us?
Majority of installation images from 2011/2012
Range of installation years begins in 2007
Installation data prior to 2007 may be missing or limited in WP databases

## Slide 14: Approach
Understand Data
  How does it look?
Most images are 400px x 400px (square). Useful for batch normalisation.
Larger images up to 6000px are likely to create issues when resized to the model’s standard resolutions of 224px or 299px (square).
Not all images are square (n px by n px). May require segmentation and to be placed into a subset (not implemented in model).
Images are assumed to all be top-down aerial imagery, however it is noted that not all images are taken from the same height. This is particularly visible in images that are not the standard 400x400px resolution.

## Slide 15: Approach
Understand Data
Exponential system size increase based on annualised data
Increased system sizes partly attributable to panel efficiency gains (W/m2)

## Slide 16: Approach
Understand Data
Unusual for
residential!

## Slide 17: Approach
sample size in these years (<100) skews the mean installation size

## Slide 18: Approach
Consider limitations
  What may create false positives?
Air-conditioning units | Vehicles | Drawn-out shadows
Pools | Pergolas | Roof-tie structures
Elevated roof sections | Solahart water-heating units | Commercial ducting
Commercial walkways | Parking spaces and driveways | Water tanks
Tarps | Trampolines | 
  The provided data is binary (PV, Non-PV)
  Binary data limits the model to a sigmoid final model layer

## Slide 19: Approach
Consider limitations
  What may create false negatives?
Rectangular images | Objects covering panels | Poorly angled panels
Lack of visible panel edges | Shade (unlikely) | 

## Slide 20: The Model
Convolutional Neural Net (CNN) model
Leverages the Fast.AI wrapper on top of PyTorch
Specifies:
  Data set to utilise
  Functions to split source data into a training & validation set
  Functions to import image meta-data
  Learning rate specification and annealing
  Data augmentation
Result accuracy based on confusion matrix output

## Slide 21: We found…
Resnet34 architecture is adequate
First training epoch (last layer only): 86.4% accuracy
False negatives generally occurred where panel edges were not visible
False positives generally occured on grid-like structures (tiles, pergolas etc)
Learning rate utilising SGDR on final layer provides small improvement: 88.6%
SGDR with differential learning rates yields significant accuracy increase
  Layers were unfrozen, and the last 3 layers were re-trained until overfitting (train loss > validation loss)
  Significant accuracy improvement (97.3%), however the risk of overfitting may be high
TTA provides small benefit: 97.8% accuracy (+0.5%)
Rectangular imagery and multi-residential imagery does require additional care, and likely image segmentation. Segmentation was not explored, as this would have formed Part B scope.

## Slide 22
Significant dropout:
  Assumed dropout would improve generalisation of solar panels and reduce false positives
Data augmentation:
  With blur – similar principle to the above – seemed to be counterproductive by reducing accuracy
  30 degree image tilt – To better generalise house (and by proxy panel) positioning – reduced the validation set accuracy
  Perhaps we were using the wrong type of augmentation?
Moving up to a ResNet50 model took far longer to train and did not yield a performance increase.
What didn’t work...

## Slide 23: We learned…
Following the basic fast.ai principles yields generally accurate CV results
Minimising data augmentation helped
Randomising the test set and validation set to check yielded model results are not a fluke
How tasks can be segmented better in the future to accelerate works

## Slide 24: What worked?
Dropout
  No dropout results in rapid overfitting – not recommended
  Default dropout of 25% (first dropout layer) and 50% (second dropout layer) in the resnet34 model worked well

## Slide 25: Challenge 2
Photovoltaic generation
PART B - SIZING

## Slide 26: Overview
Part B continues from Part A code
PV image Metadata is accessible in the Jupyter Notebook

## Slide 27: Thank you for your attention.
Team UnicorNN