## Slide 1: Western Power Hack-a-Gig
Team UnicorNN

## Slide 2: Challenge 1 – Smart Meter Data
Overview
Approach
Results
Insights

## Slide 3: Overview
To do

## Slide 4: Challenge 2
Photovoltaic generation
PART A - Detection

## Slide 5: Overview
Define requirements
  Understand task
  Analyse data
  Form an approach
  Consider limitations
  Determine deliverables
Follow to-do list (right)
Document learnings
Share insights
1
Retrieve Data
2
3
Explore Data
Prepare Data
4
Develop model
5
Assess performance
6
Submit Model

## Slide 6: Requirements (Part A)
The task
  Utilise Western Power data to develop a model which identifies distribution embedded PV generation. Target a model accuracy of >98.5%.
  Test what works, what doesn’t work – document learnings
  Assess model performance against a hold-out set
  Provide required documents

## Slide 7: Approach
Understand Data
  What is provided?
Clean Release
  High degree of assumed PV and Non-PV image labelling accuracy
  Smaller set
Extra Release
  Lower degree of confidence in labelling accuracy
  Larger set (2-4x)

## Slide 8: Approach
Understand Data
  What does it tell us?
Majority of installation images from 2011/2012
Range of installation years begins in 2007
Installation data prior to 2007 may be missing or limited in WP databases

## Slide 9: Approach
Understand Data
  How does it look?
Most images are 400px x 400px (square). Useful for batch normalisation.
Larger images up to 6000px are likely to create issues when resized to the model’s standard resolutions of 224px or 299px (square).
Not all images are square (n px by n px). May require segmentation and to be placed into a subset (not implemented in model).
Images are assumed to all be top-down aerial imagery, however it is noted that not all images are taken from the same height. This is particularly visible in images that are not the standard 400x400px resolution.

## Slide 10: Approach
Understand Data
  And have a bit of fun…
Exponential system size increase based on annualised data
Increased system sizes partly attributable to panel efficiency gains (W/m2)

## Slide 11: Approach
Consider limitations
  What may create false positives?
Air-conditioning units | Vehicles | Drawn-out shadows
Pools | Pergolas | Roof-tie structures
Elevated roof sections | Solahart water-heating units | Commercial ducting
Commercial walkways | Parking spaces and driveways | Water tanks
Tarps | Trampolines | 
  The provided data is binary (PV, Non-PV)
  Binary data limits the model to a sigmoid final model layer

## Slide 12: Approach
Consider limitations
  What may create false negatives?
Rectangular images | Objects covering panels | Poorly angled panels

## Slide 13: The Model
Convolutional Neural Net (CNN) model
Leverages the Fast.AI wrapper on top of PyTorch
Specifies:
  Data set to utilise
  Functions to split source data into a training & validation set
  Functions to import image meta-data
  Learning rate specification and annealing
  Data augmentation
Result accuracy based on confusion matrix output

## Slide 14: What worked? [First Run]
Resnet34 Architecture:
  First run with a single training epoch: 86.4% accuracy
  False negatives generally occur where panel edges are not visible
  False positives generally occur on grid-like structures
  Learning rate utilising SGDR on final layer provides small improvement: 88.6%
  SGDR with differential learning rates yields significant accuracy increase
    Tuning the 3rd last layer: Minimal accuracy improvement, model underfitting
    Tuning the 2nd last layer: Small accuracy improvement, minor overfitting
    Tuning the last layer: Significant accuracy improvement, overfitting (97.3%)
  TTA provides small benefit: 97.8% accuracy

## Slide 15: What worked?
Dropout
  No dropout results in rapid overfitting – not recommended
  Default dropout of 25% (first dropout layer) and 50% (second dropout layer) in the resnet34 model worked well

## Slide 16: What didn’t work?
Significant dropout:
  50% dropout resulted in 89.7% accuracy (↓8.1%)
  25% dropout

## Slide 17: Challenge 2
Photovoltaic generation
PART B - SIZING

## Slide 18: Overview
Part B continues from Part A code
PV image Metadata is accessible in the Jupyter Notebook

## Slide 19: Thank you for your attention.
Team UnicorNN
Sofia Sibanic
Adrian Goldberg
Sandesh Satpute
Jordan Pratt